## Slide 1: Cloud Tracking & Solar Forecasting for PV Power Prediction Project Update
Luis Domínguez, CH.RD.C1, August 30, 2013

## Slide 2: Briefing
Project Update
  Project Status
  Project Plan
Technical Progress
  VISMO operation & issues encountered
  Cloud Motion Estimation
  GHI clear sky prediction
  PV power output prediction
Next Activities

## Slide 3: Work Breakdown Structure
Cloud Tracking
Irradiance Forecasting
Hardware
Cloud Motion Estimation and Classification
Software
Validation & Testing
(WP 5)
Technical Documentation
& Reporting (WP 6)
Algorithmic Development
(WP 2)
Work Package
Tasks
IP Strategy
(WP 3)
PV Power Output Modeling (WP 4)
Prototype Development
(WP 1)

## Slide 4: Project Plan
Progress Up to Date

## Slide 5: Cloud Tracking & Solar Forecasting for PV Power Prediction Prototype Operation & Issues
Luis Domínguez, CH.RD.C1, August 30, 2013

## Slide 6: VISMO Prototype
Initial Tests 5.06.2013

## Slide 7: VISMO Prototype
Initial Tests 5.06.2013

## Slide 8: VISMO Prototype
Issue – Enclosure Overheating
Enclosure (with Paraffin included)
Camera (with Paraffin included)
Enclosure
w/o Paraffin
Camera w/o Paraffin
Camera operating temperature range

## Slide 9: VISMO Prototype
Cooling System Design
Fans
Suction Funnel
Support plate
Suction Case
Liquid CPU Cooler
Pump volume: 400 Liters/hr.
Pump rotor speed: 3600 rpm @12VDC
Fan speed: 1600 rpm
Cooler Master Eisberg 120L Prestige

## Slide 10: VISMO Prototype
+ Cooling System

## Slide 11: VISMO Prototype
Camera Temperature Control
Chart: 
| 0.62847222222222221 | 0.63194444444444442 | 0.63541666666666663 | 0.64236111111111105 | 0.64583333333333337 | 0.64930555555555558 | 0.65277777777777779 | 0.65625 | 0.65902777777777777 | 0.66041666666666665 | 0.66319444444444442 | 0.6645833333333333 | 0.66666666666666663 | 0.66875000000000007 | 0.67083333333333339 | 0.67291666666666661 | 0.67499999999999993 | 0.67708333333333337 | 0.6791666666666667 | 0.68125000000000002 | 0.68333333333333324 | 0.68541666666666667 | 0.6875 | 0.68958333333333333 | 0.69166666666666676 | 0.69374999999999998 | 0.6958333333333333 | 0.69791666666666663 | 0.70000000000000007 | 0.70208333333333339 | 0.70416666666666661 | 0.70624999999999993 | 0.70833333333333337
Camera | 38.1 | 38.7 | 39.2 | 39.1 | 38.9 | 38.9 | 39.3 | 39.3 | 39.4 | 39.4 | 42.2 | 44 | 45.9 | 46.9 | 48 | 49.1 | 50.2 | 51.1 | 51.7 | 44.3 | 42.3 | 41.3 | 40.7 | 40.2 | 39.9 | 39.4 | 39.4 | 39.2 | 39 | 38.9 | 38.7 | 38.7 | 38.7
Enclosure | 40.1 | 40.3 | 40.3 | 40.9 | 41.2 | 41.4 | 41.6 | 41.8 | 41.9 | 41.9 | 42.1 | 42.5 | 43.3 | 43.7 | 44.2 | 44.6 | 45.1 | 45.3 | 45.7 | 45.1 | 44.5 | 44 | 43.5 | 43.1 | 42.8 | 42.6 | 42.4 | 41.9 | 41.6 | 41.4 | 41.1 | 41 | 41

## Slide 12: VISMO Prototype
Roof Installation on 22.07.2013

## Slide 13: VISMO Prototype
26. July 2013:
  Water inside the prototype and also between case walls and upper spherical glass cover.
  Condensation droplets were detected on images after heavy rain.
Issue 2 – Water leakage inside camera case

## Slide 14: VISMO Prototype
31. July 2013:
  The water was removed and the prototype was dried.
  Hypothesis was that cooling water from pump was leaking. However, cooling pump water level seemed ok, indicating leakage was only due to bad weather.
Issue 2 – Water leakage inside camera case

## Slide 15: VISMO Prototype
13. August 2013:
  The water was again removed from the space between the case walls and the upper spherical glass cover.
  Cover was taped to the base body of the case to make the contact Waterproof.
  The cooling pump water level seemed ok.

## Slide 16: VISMO Prototype
16. August 2013
  Problem seems to be solved. No condensation droplets are visible on the images.
  Currently monitoring images.

## Slide 17: VISMO Prototype
Direct (Local) Connection
Network (Remote) Connection
Network Configuration Issue
VISMO
Cloud Motion Estimation & Irradiance Forecasting
LAN
Forecast
VISMO
KNX weather station
(WZ / S 1.1, WES / A 2.1)
Cloud Motion Estimation & Irradiance Forecasting
KNX weather station
(WZ / S 1.1, WES / A 2.1)
Notes: Image acquisition is
as a multi-threaded architecture. Stores the captured images on a network hard drive. Can also store in a database if required

## Slide 18: VISMO Prototype
  Database size is rapidly increasing. Images are taking up large space on laptop hard drive. These have been temporarily moved to project folder.
    Potential solution: buy an external hard drive and to use it only for storing images.
Network Configuration Issue

## Slide 19: VISMO Prototype
In the early morning the algorithm is not working properly.
  Reason: clouds are very dark, sun very bright. Detection algorithm fails to recognize clouds.
In general the resolution of the images is not so as high as expected and the images seem quite dark most of the time.
  Proposed Solution: Dynamic HDR
Some Observations

## Slide 20: VISMO Prototype
Image Acquisition, Processing & Analysis
Raw Image
Exposure Correction*
* Procedure required to minimize sun effects.
Notes:   To deal with the impact of the sun, takes several images varying exposures, and merges them to obtain the finalized image.
  On the final output, areas with and without the sun have a balanced tone. Details around the sun can easily be noticed.
  The frequency with which the images are captured can be configured using this software.
  Camera parameters such as exposure and sensor sensitivity can be configured.

## Slide 21: Cloud Tracking & Solar Forecasting for PV Power Prediction Cloud Motion Estimation
Luis Domínguez, CH.RD.C1, August 30, 2013

## Slide 22: Cloud Tracking
Object Tracking on image plane
History
Frame 1:
Cloud Tracks
Now Frame
Object Positions
Automatic detection of moving clouds in the image coming from the camera is based solely on motion.
The problem (motion-based object tracking) is divided into two parts:
  Detecting the moving cloud in each frame
  Associating the detections (i.e. tracks) corresponding to the same object over time.
After the assignment, we “update” Kalman filters of tracks, if necessary generate new traces and delete the outdated ones.
The predictions for next steps come from the “predict” method of Kalman filters.
Hungarian Algorithm
Assignment
Notes: In the first part (here), the detection of moving objects uses a background subtraction algorithm.
Morphological operations are applied to the resulting foreground mask to eliminate noise
Blob analysis detects groups of connected pixels, which are likely to correspond to moving objects.
The second part, the association of detections to the same object is based solely on motion.
The motion of each track is estimated by a Kalman filter.
The filter is used to predict the track's location in each frame, and determine the likelihood of each detection being assigned to each track.

## Slide 23: Cloud Tracking
State Estimation :
where:
and are the coordinates of the image plane,
is the area of the image object and,
, and are the corresponding derivatives.
 Integrate the change in area and position to get an estimation.
Kalman Filter Implementation
Notes: As I mentioned the motion of each track is estimated by a Kalman filter.
For now, we use straightforward implementation of the Kalman filter

## Slide 24: Cloud Tracking
For this mapping we use the calibration model of the camera.
  Calibration model provides us mapping between ‘image plane coordinates’ and ‘the coordinates on the unit circle around the camera’; and the inverse.
  We train this model using a chessboard with a standard procedure.
  Later use it to project the cloud pixels on the image plane onto a plane with real dimensions in km’s that is parallel to earth.
  In parallel we do all the tracking work on this real plane as well.
Object Tracking - Projection to real plane
Image Plane
Real-dimension model plane
Unit sphere around camera
Mapping
Notes:   So far I have talked about tracking the clouds on an image plan, to obtain the predictions in real coordinates we nee to use a calibration model for the camera.
  Calibration model provides us with a mapping between ‘image plane coordinates’ and ‘the coordinates on the unit circle around the camera’; and the inverse.

## Slide 25: VISMO Prototype
Cloud object bounding box implementation of the current version of cloud tracking algorithm does not capture the fineness needed for prediction of an occlusion.
Several cloud shapes (especially if there is a high cloud cover) are not represented well enough. The square approximation covers for example 90% of the whole area. (see next slide)
  Potential Solution: track movements of cloud fronts («corners») near the sun, e.g. front coming towards the sun
Sun and clouds appear often inside the same object. Once a cloud passed over the sun the object separates into 2 objects.
  Potential solution. Separation of objects into sun & clouds. A sun detection/tracking algorithm needs to be implemented
Some Observations (running various image streams)
Notes: The bottleneck at the moment is the missing cloud motion prediction and its translation into GHI predictions for specific points on the ground. This will be the hardest part.

## Slide 26: Vision Prototype
Image read: 2013_07_28_15_14_36_468.jpeg
Some Observations (running 2013/07/28)

## Slide 27: Cloud Tracking & Solar Forecasting for PV Power Prediction GHI Prediction
CH.RD.C1, August 28, 2013

## Slide 28: GHI Prediction
The PV_LIB Toolbox for Matlab, developed at Sandia National Laboratories. Tool mainly used for simulating the performance of photovoltaic energy systems.
Includes several Irradiance and Atmospheric functions:
  Extraterrestrial incident radiation
  Standard altitude based on air pressure
  Average atmospheric pressure
  Absolute airmass
  Clear sky global horizontal irradiance models
    Haurwizt (GHI)
    Ineichen (GHI,DNI, and DHI)
Clear Sky Model Selection

## Slide 29: GHI Prediction
Reno et al1 evaluated several clear sky models using a large set of data (300 years) and 30 different sites.
The analysis of clear sky models indicate that there is a trade-off between model complexity and implementation simplicity or practicality of obtaining input data.
The REST2 and the Ineichen models account for many of the atmospheric parameters are most accurate with an average RMSE of 5 % among several locations.
Clear Sky Model Selection
1Global Horizontal Irradiance Clear Sky Models: Implementation and Analysis. Sandia Report, SAND 2013-23389, March 2012.
Notes: This figure shows that a model with large errors at one site is also likely to have large errors at other sites, and conversely, more accurate models tend to be more accurate at each site, and that the overall accuracy of a clear-sky model is generally summarized by the average error over many sites. However, model accuracy depends fairly strongly on site elevation, with very simple models being less accurate at higher elevations.

## Slide 30: GHI Prediction
REST2 is a complex two-band model requiring a large number of atmospheric parameters, such as station pressure, ground albedo, aerosol optical depth, albedo reduced ozone vertical path lenght, Angstrom’s turbidity, etc.
Ineichen model relies on a gridded dataset (look up table) that varies by month and location, but the model does not need other site-specific data, so is easy to implement.
Haurwitz model is also a simple model and is easy to implement but its performance is found to be lower than Ineichen.
In conclusion, the Ineichen model was selected for predicting GHI in clear sky conditions.
Clear Sky Model Selection

## Slide 31: GHI Prediction
Why?
  Poorly calibrated sensors may report systematically low readings.
  The Largest error between clear sky models and measured data can come from sensor calibration issues (i.e. miscalibration) or from incorrect clear sky constants such as altitude.
The clear sky model will provide the shape (irradiance curve) that is expected in each day for the location in which the data was collected .
Adaptation of Clear Sky Model to Data

## Slide 32: GHI Prediction
Automatic detection of clear sky days
  Computation of statistics (criteria) over a moving windows of data points.
    Irradiance average
    Maximum irradiance value
    Length of line connecting the points in the time series
    Variance of slope
    Maximum deviation of slope
The identification of a data scaling factor ().
Adaptation of Clear Sky Model to Data

## Slide 33: GHI Prediction
The identification of a data scaling factor () is obtained by solving a minimization problem involving the RMSE between the measured GHI and the clear sky irradiance (CSI) model output:
Adaptation of Clear Sky Model to Data
Detect Clear Sky Times
Input Data (GHI)
Fit Model to Clear times
Scaling Coefficient ()

## Slide 34: GHI Prediction
Clear Sky Model
Data
Clear Sky (Ineichen)

## Slide 35: GHI Prediction
Clear Sky Model
 = 0.9264
Scaling Factor:
Data
Clear Sky (Ineichen)
Identified Clear Sky Data

## Slide 36: Cloud Tracking & Solar Forecasting for PV Power Prediction PV Power Output Prediction
CH.RD.C1, August 30, 2013

## Slide 37: Modeling PV Power Output
Static Model:
Assumptions: ,
Constant ambient temperature.
Least-Square fitting day-by-day:
Variation of Coefficients:
Day-by-day fitting

## Slide 38: Modeling PV Power Output
Clear sky day
Partially cloudy day
Day-by-day fitting

## Slide 39: Modeling PV Power Output
Variable day
Very cloudy day
Day-by-day fitting

## Slide 40: Modeling the PV Power output
Conclusion:
The simple model performs well, nevertheless the inaccuracy greatly increases for very variable days
Model structure seems to capture the relevant behavior
Parameter adaptation might help given an actual window of GHI and PV output data
Simple idea:
Use a KF to estimate the parameters on the past data window (e.g. 2 hours of past data)
Then assume constant parameters for the future and use the KF to predict the PV output given a GHI prediction vector (e.g. 15min)
Day-by-day fitting

## Slide 41: Modeling the PV Power output
KF Model:
States: with static evolution:
Output Equation:
Output:
Inputs:
Algorithm:
Kalman Filter is used to estimate the parameters at every time step given and .
This is fine for a passed history window of N stored data.
When the next M predictions are given (e.g. by the Vision algorithm) the parameters are assumed to remain constant.
Kalman Filter Approach

## Slide 42: Modeling the PV Power output
Algorithm:
Kalman Filter Approach
KF
Last N points
predicted next M points
Last N points
predicted next M points
Last N points
+
future
VISMO cam
Vision Algorithm
Cloud detection Classification Motion prediction GHI Prediction
+
Take action
Clear Sky GHI Model

## Slide 43: Modeling PV Power Output
Some Results:
Kalman Filter Approach
Clear Sky forecast
KF PV power prediction for the next 15min
Kalman Filter

## Slide 44: Modeling PV Power Output
Some Results:
Kalman Filter Approach
«Artificial» Vision forecast
KF PV power prediction for the next 15min
Kalman Filter

## Slide 45: Modeling PV Power Output
Conclusions:
The presented approach works well and is able to predict into the future.
Once a GHI 15min forecast is available from the cloud tracking algorithm, PV power output predictions can be obtained.
Kalman Filter Approach

## Slide 46: Cloud Tracking & Solar Forecasting for PV Power Prediction Next Activities
CH.RD.C1, August 28, 2013

## Slide 47: VISMO System
Weather Data
PV Measurement Data
Camera
Processed and compressed images
Shared File System
Cloud Tracking
PV System Database
Clear Sky Model
Weather Database
GHI Estimation with Cloud Tracking
Cloud Motion Model
Weather Data
PV Plant Model
PV Power Output Predictions
Overview & Target
GHI Drop Estimation
Image Acquisition
GHI Estimation

## Slide 48: Next Activities
Refine object detection and localization:
  Image processing part (refine size and position estimation of individual objects)
  Existing solution groups all objects: sun and clouds into a single bounding box.
    When cloud is close to sun, brightness of cloud is consider as the sun.
    Rectangular boxes too big for estimating impact of clouds.
Object characterization (e.g. cloud features and magnitude of GHI estimation)
Take object motion prediction into account (time and partial shading effects) for GHI prediction and shadow localization.
Carry out Case Studies
Summary

## Slide 49: Case Study 1
Clear Sky Days + Irradiance drop due to Fast Clouds
11:53:04
11:53:55

## Slide 50: Case Study 1
Clear Sky Days + Irradiance drop due to Fast Clouds

## Slide 51: Case Study 2
Overcast Days + Irradiance variation due to sky condition
11:19:13
11:46:52

## Slide 52: Case Study 2
Overcast Days + Irradiance variation due to sky condition

## Slide 54
IDs:
FFs:
Strategic:
Vision-based Sky Monitoring (VISMO) System
Project Status
Objective
  To build a sky monitoring prototype system with cloud tracking and solar forecasting capabilities for improved grid operation of PV systems.
Achievements
  Ramp rate analysis of PV Power Generation in CHCRC.
  Identification and adaptation of a clear sky model to predict GHI clear sky days in Baden-Dättwill.
  First implementation of a cloud tracking algorithm (Kalman Filter based)
  Prototype test-bed has been built and is currently in operation (07/2013)
Project Value
  Increase power capacity penetration of PV systems.
  Smooth power generation - optimal operation via ramp rate control
Technical Challenge
  Automated cloud classification requires extensive data collection (training library).
  The analysis of images requires the implementation of post-processing algorithms (e.g. cloud detection, binarization and background subtraction) which may loose important information from the images. The question is how to postprocess the images without loss of iformation
  Solar and cloud forecasting requires the evaluation and implementation of different type of models (e.g. clear-sky index combined with NAR, NARX models). Measurements can be used to build black-/gray-box, statistical or artificial intelligence based prediction models
Status of Project
  Currently generating sky image database for advanced algorithms. Next step is to validate the system performance and iteratively improve the cloud tracking algorithm
  ID submitted for review.
Issues
  Hardware prototyping taking longer than expected – cooling and leaking issues
  Activity new to group. Background of team is limited – extensive research and learning
  Unavailability of Intern from mid July to Mid September. Burak Zeydan returns as Master’s Student.
  Unavailability of project team members.
Gate Status
Business Case
Main Risks (Top 3)
High cost of components
Relative inexperience in the area of computer vision.
Resource constraints
TD
Savings MUSD | New. rev. MUSD | NPV MUSD | IRR % | Payback years
xx | xx | xx | xx | xx
CF kUSD | BU kUSD | PTD kUSD | ETC kUSD | EAC kUSD
324 | xxx | xxx | xxx | xxx
Project Financials
Organization & Resources
Funding program: AGI
CRID: 21174
Executing CRC: CH
Project Manager: Luis Dominguez
BU/LBU: PSPG
BU contact: Celine Mahieux
IP Status
First Discussions
Jan/2013
Gate 4
Jan/2014
April/2013
Gate 2 Concept Ready
0
1
2
3
4
5
6
IP comments
Last gate: G0 / 2012
Next gate G1 / Jan 2013
G5 date: TBD

## Slide 55: Project
Overview of Past and Future Activities
IP Documentation & Technical Reports
VISMO Technical Option Report
Presentation
Ramp Rate Analysis @ CHCRC
Matlab access code to KNX database
Image Database Generation
Luis: 1.0 MY Mehmet: 0.3 MY Andrea: 0.7 MY
now
Jan 2014
LD
BZ,LD, AC
AC
LD
LD
Cloud Motion Estimation & Prediction
PV Power Output Modeling
Ground Mapping
GHI Clear Sky Modeling & Data Analysis
BZ, LD, AC
BZ
LD
Fully Functional Prototype
Model Integration & Validation
Development of Algorithms
Data Acquisition
ID on Cloud Tracking
LD, MM,AC
IP Strategy Report
Future Tests
Test Report

## Slide 56: Clear Sky Days Identification
    Irradiance average
    Maximum irradiance value
    Length of line connecting points in time series
Notes: The second figures illustrates examples where the mean value of the measured time series is the same as under clear sky. Figure a is an example where the sky gradually and uniformly brightens, and Figure b shows a more realistic case where cloud enhancement originally increases the irradiance before the cloud occludes the sun. The simplest way to distinguish these conditions from clear-sky conditions is to also look at the maximum irradiance value M in the time series, which is our second criterion:
Three other criteria are proposed to more closely look at the differences between the shape of the measured irradiance timeseries and the corresponding clear sky model. Specifically, these criteria are intended to distinguish a variable time series, such as would result if clouds were present, from a smoothly changing time series.
Variability in irradiance resulting from the effects cloud cover, both large and small, will visually change the shape of the irradiance relative to a clear-sky profile. However, because cloud size, transparency and speed vary, the effects on the time series of irradiance also vary. Figure 8 shows two examples of variability in the measured data that do not change the mean and max of the timeseries. Figure 8a represents a small thick cumulous cloud, and Figure 8b represents high wispy cirrus clouds. The third, fourth and fifth criteria quantify aspects of variability in order to detect variability resulting from different types of clouds.
The third proposed criterion measures variability in irradiance by the length L of the line connecting the points in the timeseries (Eq. 60).
Any variability in the measured irradiance will increase the length of the line and be detected.
The fourth criterion is the variance of changes in the time series; specifically, the normalized standard deviation σ of the slope (x) between sequential points in the series.

## Slide 57: Clear Sky Days Identification
Maximum deviation from clear sky slope
Slope variance of series
Notes: However, the line length for a time series with a few, large changes, or with many small changes, may be similar to that of a smooth curve, necessitating additional criteria.
The fourth criterion is the variance of changes in the time series; specifically, the normalized standard deviation σ of the slope (x) between sequential points in the series. While this criterion cannot easily detect situations such as Figure 8b if the slope between measurements varies slightly, Figure 9 shows a scenario where the line lengths are the same, but the variance of slope criterion (i.e., the fourth criterion) will easily distinguish between clear and cloudy periods with these features.
The last criterion for detecting variability in the shape of the irradiance measurements is maximum deviation from clear sky slope, S . During a clear-sky period, the slope between each
measurement should be similar to the slope under a clear sky. Figure 10 shows a real example of measured GHI during and after a cloud passes over an irradiance sensor. At measurement 1, the
cloud is between the sun and the sensor, but by measurement 2, the cloud’s shadow has moved away from the sensor. Because the slope of measured GHI between observations 1 and 2 is
much larger than the slope between the corresponding clear-sky GHI values, the fifth criterion identifies the period including measurement 1 as cloudy. This last criterion ensures that
successive periods with cloud shadows occurring on the period boundaries are classified as cloudy rather than clear. The slope between measurements should not vary more than the error
for the given sensor.

## Slide 58: Cloud Tracking
Kalman Filter Improvement
Frame
Predict +
Predict
Frame
Prediction
Type Estimation
Kalman Estimation
Prediction Improvement +n
Kalman Estimation
weighted average of Kalman filter and the type specific model
Planned Future Work
Current Implementation
ABB Internal use only
Confidential
Notes: So the current implementation, we use the Kalman filter to predict the centroid of each track object in the current frame, and update its bounding box accordingly.
In a future work, we consider improving the Kalman predictions with additional information.
This can be in the form of cloud-type-specific noise parameters for the Kalman Filter, or a separate model to be superposed with the existing one.
For this, we are planning to use the database we are going to assemble to extract the statistical cloud-type-specific information.

## Slide 59: Cloud Tracking
Predicting the “time of impact” or “cloud arrival time”
Frame
Predictions for frame + 10 (0.5 min)
Predictions for frame + 100 (5 min)
…
ABB Internal use only
Confidential
Notes: For the estimation of arrival time in which a cloud will start occluding the sun and project a shadow over a given PV plant we use the predictions of the tracks obtain with its corresponding Kalman filter.
and evaluating the occlusion for each step.

## Slide 60: VISMO Prototype
Forecasting Strategy
2. Cloud Characterization and Motion Estimation
1.- Image/data Acquisition and Processing
3. Irradiance Estimation
Cloud velocity & arrival time
Duration of drop/increase in GHI/PV output (time to cover field array)
Magnitude of drop/increase in GHI/PV output (given by the cloud characteristics such as type and brightness level)
GHI estimation for current day/time
Expected Output
Current sky state (clear sky, overcast, partly cloudy (scattered) cloudy (broken), etc.)
Library of sky images for training & validation of algorithm
Notes: able: Sky Condition Codes
Sky Code
Description
0 clear sky, few clouds
1 Partly cloudy (scattered) or variable sky
2 Cloudy (broken) or overcast
3 Rain
4 Fog or smoke
5 Fog or smoke
7 Snow
8 Showers (intermittent rain)

## Slide 61: VISMO Prototype
Irradiance Estimation & Forecast
Collect images
Feature Extraction
<> = mean of values of window centered at X.
Var() = variance of values of window centered at x
x
Window size (neighbours)
Collect measurements
Processing
Data Acquisition
Database
GHI Data
Current Day/Time Forecast
start
k < kmax
end
No
yes
Learning Algorithm
Training and Validation sets

## Slide 62: VISMO System
Goal: On-line Implementation of Forecast
past
Horizon t
Horizon t+1
future
Predicted value y(t+k│t)
t
t-1
t+1
t+m
t+p
t-m
t-p
Measured value y(t+k)
Moving window t
Moving window t+1
Continuous Monitoring:
  Continuously monitor real-time measurements of irradiance and power output.
  Display values of the prediction at a sampling time specified by the user (e.g. every minute).
  Track the forecasting errors so as to maintain the forecasting accuracy (e.g. specified % MSE, forecasting skill index, etc.) required by the application and/or specified by the user.
Short-term Prediction:
  Moving window of predictions, updated at a specified time interval (e.g. 1 to 5 min) (this is required as the errors are expected to increase as the end of horizon is approached) .
  The specified horizon forecast length can vary from 10-30 min to 1 hour.
  The forecasting algorithm will take into account previous forecasts (from internal or external sources), current and previous measurements as well as the errors of the predictions to refine the expected accuracy for the specified horizon.

## Slide 63: VISMO Application
Ramp Control
t (min)
P (W)
dt =1min
-
+
String 1
String 2
String 3

## Slide 64: Potential VISMO Contribution
PV/Battery Integration
Estimator
Optimizer
PV/BAT System
Model
Process Controller
++
-+
Predicted output
error
Controlled output
State
Control Input
Optimized Input
State
MPC
VISMO Input
Irradiance forecast
Load Profile, Elec. Prices, etc.
Other Inputs
Parameters

## Slide 65: VISMO Application
Ramp Control
String 1
String 2
String 3
t (min)
P (W)
dt =1min
t (min)
P (W)
dt =1min